# Weather Exam Gouge for Capt. Sadler’s class

1] Know the Tri-Cellular Theory Diagram.

2] Know how to convert gradient wind to surface wind

- First step is to assign the gradient wind a cardinal point associated number.

- Second step is to subtract 45 deg from it

- Next give surface wind a cardinal point on the compass. (N, S, E, W or combo)

3] Define tropopause

- Transition zone between the troposphere and the stratosphere; temp. is isothermal with altitude; an abrupt change in rate of temp. decrease with increasing altitude marks this boundary; it’s a region not a layer

4] Calculate sea level pressure

- Example:

- Given: Station Pressure = 27 inHg and Field Elevation 1500 ft

- Find RAS

- Known: 1 inHg decrease per 1000 ft

- So: 1.5 inHg decrease per 1500 ft

- Station Pressure is above Sea Level so we add 1.5 in Hg to 27 inHg to get Sea Level Pressure

- Seal Level Pressure = 28.50 inHg

5] Know all 3 types of math problems

Type 1 Average Lapse Rate:

- Given: Point A ( temp = +2 deg C	Altitude = 6000 ft

- Given: Point B ( temp = -8 deg C	Altitude = unknown

- Find: Altitude at Point B

- Change in Temp from A to B is –10 deg C

- Temp decreases 2 deg C / 1000 ft

- So, 10 deg C will occur in 5000 ft

- Point B has a lower temp so it is higher

- Add 5000 ft to Point A altitude of 6000 ft

- Altitude at Point B is 11000 ft

## Type 2 Reported Altimeter Setting

- Given: Station Pressure = 28.20	Elevation = 4000 ft

- Find RAS

- Known: Pressure decreases 1 inHg/1000ft

- So, Pressure decreases 4 inHg/4000ft

- Add 4 inHg to station pressure to get RAS

- RAS = 32.20 inHg

Type 3 Pressure Change vs. Altitude

- Given: Point A ( Pressure = 29.50 inHg

- Given: Point B ( Pressure = 31.25 inHg		Elevation 1800 ft

- Given: Assigned altitude = 4000 ft

- Find: True Altitude at Point B?

- Sing ditty: Hi to Low look out below, Low to Hi look up to the sky.

- Choose appropriate relationship. In this case Low to Hi, so aircraft above altitude.

- Change in Pressure is 1.75 inHg

- 1.75 inHg occurs in 1750 ft

- Known: Assigned altitude = 4000 ft

- So: since aircraft is above altitude, true altitude is higher

- Add 1750 ft to 4000 ft

- True Altitude = 5750 ft

- Find: AGL altitude over Point B?

- Known: Elevation = 1800 ft

- Thus, ground level is 1800 ft

- Subtract 1800 ft (elevation) from your true altitude

- AGL altitude = 3950 ft

- Find: What does altimeter read at landing?

- Change in Pressure is 1.75 inHg and produces a change of 1750 ft on your altimeter if you do not Kohlsman adjust

- Known: Aircraft is above altitude

- Aircraft elevation is 1800 ft

- Subtract Pressure Change over 1750 ft from 1800 ft

- Altimeter reads 50 ft.

6] What 3 elements are associated with moisture?

- Clouds

- Humidity

- Precipitation

7] What kind of drifts are associated with a high pressure area?

- High pressure area, winds flow clockwise.

- Fly into a high, you get right cross wind and left drift

8] What two forces cause winds to travel parallel to isobars?

- Coriolis Force : bends gradient winds to the right, do not affect surface wind because of friction

- Pressure Gradient Force : initiating force for all winds

9] Humidity definitions

# Relative Humidity : percent of saturated air

- Specific Humidity : Ratio of water vapor per unit mass of air. The higher the dew point the higher the specific humidity.

10] Difference between relative humidity and specific humidity

- Relative Humidity measures the percent of saturated air or what percentage of the bucket is filled with water

- Specific humidity measures how much water vapor is contained per unit mass of air or  how much water is in the bucket.

11] Two types of weather conditions that cause icing

- Supercooled water (freezing rain)

- Wet snow

12] Know all 4 lifting actions and differentiate b/w them

- Convergence : winds meet, cause air to move vertically

- Orographic : wind runs into terrain, can’t go through, so it lifts air

- Frontal : front moves in, so air has to move up

- Thermal : sun heats land, land gives off heat, warm air rises

# 13] What are the three types of stability?

- Stable : Air is pushed up until lifting action is removed, air is colder than the surrounding air, so it falls to its original position

- Unstable : Air is pushed up until lifting action is removed, air is warmer than the surrounding air, so it is pushed up and continues to rise

- Neutral : Air is pushed up until lifting action is removed, air is the same temp as the surrounding air and therefore it remains in place

14] Given lapse rate, state flight conditions or vice versa       ***

Lapse Rates				Stability

Steep					Unstable

Shallow Moisture			Unstable             ** Know as Conditional Instability

Shallow Dry				Stable		   ** Know as Conditional Instability

Iso/Inversion				Stable

Flight Conditions		Stable Atmosphere		Unstable Atmosphere

Cloud type			Stratus				Cumulus

Turbulence			Smooth			Rough

Visibility			Poor				Good (outside of clouds)

Winds				Steady				Gusty

Precipitation			Steady				Showery

Icing				Rime				Clear

Air Mass			Warm				Cold

Front				Warm				Cold

# 15] What are the two types of shallow lapse rates?

- Dry : temp. decreases 3 deg C / 1000 ft altitude increase

- Moist : temp. decreases 1.5 deg C / 1000 ft altitude increase

16] Define air mass

- A large body of air that has essentially uniform temp. and moisture conditions in a horizontal plan.

- Source region never changes

17] Maritime vs. Continental

- Maritime source region is most likely to produce clouds

18] Temp. in relationship with air and land

- Air temp is relative to surface below it

- Summer time, air masses are cold

- Winter air masses are warm

19] Three parts of air mass classification

- First is source region. A, P, T, E (Arctic, Polar, Tropical, Equatorial)

- Second is surface of their source region. m or c (Maritime or Continental)

- Third is temp. k (cold) or w (warm)

20] How to you get from Maritime to Continental?

- m to c let out moisture

- c to m need precipitation

21] Describe the two types of occlusions

- Occlusions have three airmasses and two fronts

- Left side is behind, right side is ahead

22]What are the general conditions of occlusions?

- Combination of warm and cold fronts

23] Define Squall Line

- A non frontal line of violent thunderstorms

- Indicated by purple, dotted, dashed line

24] What is the worst hazard of squall line or thunderstorm?

- Turbulence

25] What are the worst hazards of squall lines or thunderstorms?

- Primary : turbulence

- Secondary: hail

26] Know requirements for thunderstorm development

- L		Lifting : most likely convergence

- U		Unstable air

- M		Moisture content in the air

- B		Building clouds through the freezing level

27] Order of precedence when flying around thunderstorm

- Go around

- Fly over the top

- Fly below

- Fly through the lower 1/3

28] What weather conditions form tornadoes?

- Marked convective instability

- Pronounced horizontal wind shear

- Rapid moving cold fronts or squall lines

- Strong convergence

29] What is convective instability?

- Dry air over Moist		-    Moist air over Dry

30] Everything about microburst

Definition: intense highly localized downdraft

4 Main Characteristics:

- May emanate from any convective cloud

- 2000 ft to 6000 ft per min downdraft

- Occur mid-afternoon in the summer months

- Last 5 to 10 minutes

### Detection

- Visual cues : virga, dust, rain shafts w/ rain diverging from the core of the cell, roll clouds, lightning, torrential heavy rain showers

- Wind Shear Alert Systems : NEXRAD, DOPPLAR, LLWAS (low level wind shear alert sys)

- PIREPS : pilot reports

- Departure / Arrival Weather Reports

### Sequential Effects: what the aircraft will feel/do as it enters/leaves microburst

Entering:

- First: Increase in Headwind

- Second : Increase in AOA

- Third : Increase in IAS

Leaving:

- Fourth : Increase in Tailwind

- Fifth : Decrease in AOA

- Sixth : Decrease in IAS

31] What is mechanical turbulence?

- Any irregular terrain. Could be mountains, buildings, whatever

32] Know everything that forms CAT and define CAT

- Clear Air Turbulence: a non-convective form of windshear turbulence

- Formed by jet streams

- Formed by surface inversion                  ** all three are not required to form a CAT

- Formed by mountain wave

33] Classifications of Turbulence		34] Classifications of Icing

- Light 					-   Trace

- Moderate					-   Light

- Severe					-   Moderate

- Extreme					-   Severe

35] Define wind shear

- Sudden change in wind direction and or speed over a short distance

36] What weather conditions form frost?

- L	Little or no wind

- L	Lack of clouds

- A	AOT below freezing (temp)

- D	Dew point within 5 deg C of air temp

37] At what temp does structural icing occur?

- Below 0 deg C

38] What kind of ice does freezing rain cause?

- Clear

39] What causes greatest change in Altimeter, Air Speed, and Rate of Climb?

- Icing is greater than pressure

- Affects are due to Pitot-Static clogs

40] Two types of fog and how to get it or get rid of it

### Radiation Fog

Get it by: 	Nocturnal or radiation cooling beginning around 1530

Get rid of it: 	Sunrise

Winds greater than 10 knots

### Steam Fog

Get it by:	Cold air over warm water

Get rid of it:	Dissipates by heating the air through conduction

Winds greater than 10 knots

41] Visibility Definitions

Visibility: the ability to see prominent unlighted objects by day and prominent lighted objects by night, expressed in statute miles.

Flight visibility: average forward horizontal distance measured in SM from the cockpit in flight

Prevailing visibility: greatest forward horizontal visibility, SM, equal or exceeded throughout at least half of the horizon circle, which need not be continuous

Runway Visual Range: horizontal distance a pilot will see by looking down the runway from the approach end

Slant Range visibility: distance on final approach when you can see the runway

Obscuring Phenomena: any collection of particles which will reduce horizontal visibility to less than 7 SM

Ceiling: height AGL to the lowest broken or overcast layer, or the vertical visibility into an obscuring phenomena

Vertical visibility: distance seen directly upward from the ground level into an obscuring phenomena

42] What causes saturation?

- Cooling temp to dew point

- Evaporations brings dew point to temp (adds moisture to air)

43] Sky coverage chart

Classification		Meaning		Sky Coverage

SKC			Sky Clear		0/8

FEW			Trace			0/8 to 2/8

SCT			Scattered		3/8 to 4/8

BKN			Broken			5/8 to 7/8

OVC			Overcast		8/8

VV			Vertical Visibility	8/8 (surface based: 0 to 50 ft only)