- Any operating procedure, practice or condition that may result in injury or death if not carefully observed and followed.

  - Note

  - Warning

  - Caution

  - Procedure

- Max gross weight for takeoff.

  - 3200

  - 3100

  - 3300

  - 3250

- Max weight capacity of cargo hook.

  - 2000

  - 1800

  - 1000

  - 1500

- __________ denotes urgency to land at first safe landing site.

  - Land immediately

  - Land as soon as practicable

  - Land as soon as possible

  - Land whenever you want

- __________ will be used when a procedure is recommended.

  - Shall

  - Will

  - May

  - Should

- The tail boom is a __________ structure made of aluminum alloy.

  - Internal frame

  - Partial monocoque

  - Semi- monocoque

  - Full- monocoque

- What instrument measured the difference between impact air pressure from the pitot tube and static air pressure from static vents?

  - VSI

  - Airspeed indicator

  - Barometric Altimeter

  - Radar Altimeter

- The Cargo Hook assembly is attached so that weight lifted is in line with the main rotor causing no change in the Center of Gravity(CG).

  - True

  - False

- Illumination of the SPARE caution light during flight is treated as ___________.

  - Land as soon as practicable.

  - Land immediately

  - Land as soon as possible

  - Continue normal operation.

- __________ is used to indicate to indicate futurity and does not require application of a procedure.

  - Shall

  - Will

  - May

  - Should

- The restraint harness locks automatically at ____ to ____ G’s.

  - 2 to 3

  - 1.5 to 3

  - 1 to 2

  - 1 to 2.5

- __________ denotes a serious condition.  Landing in trees, water or unsafe areas should be considered a last resort.

  - Land immediately

  - Land as soon as practicable

  - Land as soon as possible

  - Land whenever you want

- The vertical fin is a __________ structure made of aluminum honey comb and aluminum skin.

  - Internal frame

  - Semi-monocoque

  - Full- monocoque

  - Partial-monocoque

- Gas temperatures displayed on the TOT gauge are read

  - Between the compressor and combustion sections

  - In the combustion section

  - Between the gas producer turbine and the free power turbine

  - By four thermocouples located in the exhaust collector

- When the anti-icing system is on, hot air is provided to the

  - Compressor front support

  - Axial compressor

  - Centrifugal compressor

  - Entire compressor section

- Max oil temp is _____ degrees celcius.

  - 98

  - 100

  - 105

  - 107

- Hot air for the anti-icing system comes from the

  - Compressor section

  - Combustion section

  - Turbine section

  - Heater at 12 o’clock position on front of engine

- Minimum Ng during normal operations is

  - 60

  - 90

  - 98

  - 100

- Thermocouples which measure TOT are located

  - In each exhaust stack

  - On the outer case of the combustion section

  - In the combustion liner

  - Between the Nf and Ng turbines.

- During power transits, TOT may be 810 to 843 degrees Celsius for a max of

  - 5 min

  - 5 sec

  - 6 min

  - 10 sec

- The squirrel cage fan provides cool air for the oil cooler and is powered by the

  - Electrical system

  - Hydraulic system

  - Accessory gearbox

  - Tail rotor drive shaft

- _______% of air passing through the combustion chamber is for cooling.

  - 50

  - 66

  - 75

  - 80

- The Allison 250-C20J is derated to __________ HP.

  - 300

  - 310

  - 317

  - 325

- Minimum engine oil pressure from 79%-94% Ng is ______ psi.

  - 50

  - 90

  - 100

  - 115

- Red TOT light illuminates if temp exceeds _______ degrees Celsius.

  - 738

  - 810

  - 843

  - 927

- Max TOT during normal operations is _______ degrees Celsius.

  - 738

  - 810

  - 843

  - 927

- During normal power transients, Nr may reach 114 for

  - 5 min

  - 5 sec

  - 6 sec

  - 10 sec

- Max torque during normal operation is

  - 60

  - 85

  - 90

  - 100

- What component of the TH-57 fuel supply system increases fuel pressure to between 650-700 psi.

  - In line recirculating pump

  - Forward boost pump

  - Aft boost pump

  - Engine fuel pump

- Fuel pump caution light will illuminate if fuel pressure falls below ____ psi.

  - 10

  - 5

  - 4

  - 3.5

- What is the max fuel pressure permitted during closed circuit (pressure) refueling of the TH-57?

  - 75

  - 85

  - 30

  - 40

- The fuel low caution light first illuminates when there is less than ____ gallons of fuel remaining in the fuel cell.

  - 10

  - 16

  - 18

  - 20

- If both fuel boost pumps fail, at what altitude will in-line fuel vaporization occur?

  - 2000

  - 3000

  - 5000

  - 6000

- The FCU receives fuel at what pressure?

  - 4-30

  - 100-300

  - 450-550

  - 650-750

- The engine driven fuel pump and filter assembly are located on the

  - Forward right side of the engine firewall

  - Forward accessory take off gear of the transmission assembly

  - Forward right side of the power accessory gear box

  - Aft port side of the accessory gear box

- The airframe fuel filter is located in the engine compartment

  - On the left side of the forward firewall

  - On the right side of the aft firewall

  - On the right side of the forward firewall

  - On the left side of the aft firewall

- What component automatically stops flow of fuel when the fuel cell reached capacity during pressure refueling?

  - FCU

  - Shut off valve

  - Closed circuit receiver

  - Fuel fill metering switch

- Excess fuel at the fuel nozzle is returned to the

  - Fuel cell

  - Engine driven pump by the shut off valve bypass switch

  - Engine driven pump by the FCU

  - Airframe mounted filter bowl

- The low fuel caution light illuminates when fuel reaches what level?

  - 10 gal

  - 15 gal

  - 20 gal

  - 25 gal

- The engine driven fuel pump discharges fuel at a pressure of ______ psi

  - 35-50

  - 125-150

  - 450-600

  - 650-750

- Illumination of the airframe fuel filter lite indicates

  - Inlet fuel pressure has dropped below 35 psi

  - Outlet fuel pressure has dropped below 35 psi

  - Impending bypass of the A/F fuel Filter

  - A failure in the FCU

- Fuel flow is controlled by the pilot using

  - And electrically operated valve mounted in the fuel cell

  - An electrically operated shut off valve

  - A mechanically driven bypass valve on the engine driven fuel pump

  - A mechanically driven shut off valve

- Boost pump pressure is relayed to the cockpit pressure gauge by

  - Fuel pressure transducer

  - Fuel pressure bypass switch

  - Electrical pressure meter

  - Mechanical pressure meter

- The TH-57 fuel cell is

  - Dual bladder cell with 91 gal capacity

  - Single bladder crash resistant cell with 76 gal capacity

  - Single bladder self sealing cell with 91 gal capacity

  - Crash resistant with 91 gal capacity

- In the event of a boost pump failure a pilot should not pull the C/B’s to identify which pump failed until below

  - 4000’ PA

  - 4000’ MSL

  - 6000’ MSL

  - 6000’ PA

- The transmission oil pump drive shaft also drives which of the following components in the accessory gear drive?

  - Pressure regulating valve and oil cooling fan

  - Hydraulic oil pump and Nr tach gen

  - Spray jets and oil cooler

  - Ng and Nf turbines

- The barbell shaft is located between what components of the TH-57?

  - Engine and transmission

  - Transmission and rotor mast

  - Transmission and tail rotor drive shaft

  - Ng and Nf turbines

- The last step in sprag clutch slippage emergency procedures is if the sprag clutch re-engages is to

  - Land immediately

  - Land as soon as practical

  - Land as soon as possible

  - Continue normal flight

- What are the two functions of the tail rotor gearbox?

  - Provide geared increase and 45 degree directional change

  - Provide geared increase and 90 degree directional change

  - Provide geared decrease and 45 degree directional change

  - Provide geared decrease and 90 degree directional change

- The main transmission uses what type of lubrication system?

  - Splash type

  - Wet sump/pressure*

  - Dry  sump/pressure

  - Pressure type

- The OIL TRANS PRES caution light illuminates when oil pressure falls below

  - 30 psi

  - 32 psi

  - 34 psi

  - 35 psi

- What type of lubrication system does the tail rotor gearbox use.

  - Spray jet

  - Splash type

  - Forced pressure

  - Submerged

- How many hanger bearings support the 6 tail rotor drive shaft?

  - 1

  - 5

  - 6

  - 7

- The barbell shaft provides for a flexible connection between the engine and transmission.

  - True

  - False

- In the event of high or low transmission oil pressure the pilot should

  - Land as soon as possible

  - Land as soon as practicable

  - Land immediately

  - Continue normal operations

- In the event of high transmission oil temperature the pilot should

  - Land as soon as possible

  - Land as soon as practicable

  - Land immediately

  - Continue normal operations

- The tail rotor drive shaft rotates at _________ RPM and is reduced to approximately _______ RPM and 100% Nr.

  - 5000, 1854

  - 4000, 1554

  - 6000, 2554

  - 4500, 2300

- What is the transmission oil temperature gauge protected by in the TH-57?

  - XMSN OIL TEMP C/B

  - XMSN IND relay

  - Transmission oil temp circuit breaker

  - Engine XMSN IND C/B

- In addition to indication from the dual tachometer, barbell shaft failure may also be determined by

  - Right yaw and vibration

  - Left yaw and loud noise or bang

  - Low freq vibration

  - High freq vibration

- The oil transmission pressure caution light is electrically protected by what type of device?

  - On/Off switch

  - Relay

  - Fuse plug

  - C/B

- The transmission chip light illuminates when metal particles contact the chip detector in the free wheeling unit.

  - True

  - False

- What type of materials are the drive shafts aft of the oil cooling fan rod made of?

  - Cast magnesium

  - Steel

  - Aluminum

  - Titanium

- What component is used to dynamically balance the tail rotor?

  - Static Stop

  - Balance wheel

  - Pitch change horns

  - Cross head

- Moving the collective upward causes which component to move downward?

  - Collective lever

  - Rotating swashplate

  - Unibar and pivot sleeve assembly

  - Hydraulic servos

- How is the yoke mounted to the splined trunion?

  - Tension torsion strap

  - Latch bolt

  - Yoke retention bolt

  - Pillow blocks

- How is the tension torsion strap attached to the inboard part of the yoke?

  - Latch bolt

  - Through bolt

  - Retention cap and pin

  - Pillow block

- What component receives input from the pitch control tube and causes the blade grips to change pitch?

  - Pitch change horns

  - Tension torsion strap

  - Yoke assembly

  - Splined trunion

- What connects the blade grip to the tension torsion strap?

  - Through bolt

  - Latch bolt

  - Retention cap/pin

  - Pillow blocks

- The tail rotor is a two blade __________

  - Semi-rigid

  - Semi-articulated

  - Fully-articulated

  - Rigid

- What component is responsible for maintaining high rotational inertia for auto rotations?

  - Tension torsion strap

  - Yoke assembly

  - Blade weights

  - Blade doublers

- Applying left anti-torque pedal will _______ tail rotor pitch.

  - Increase

  - Decrease

  - No effect

  - Don’t know

- The collective control stick uses a

  - Collective brake

  - Force trim button

  - Star wheel adjuster

  - Friction adjuster

- What provides the flapping axis for the main rotor?

  - Splined trunion

  - Yoke

  - Mast

  - Tension torsion straps

- How is the tension torsion strap attached to the inboard part of the yoke?

  - Latch bolt

  - Through bolt

  - Retention cap and pin

  - Pillow block

- What is retreating blade stall?

  - When forward airspeed reduces rotational flow to the point which the retreating blade operates beyond it’s critical stall angle

- What does the tension torsion strap do?

  - Absorbs centrifugal force and loads and twists to pitch angles.

- The blade grips are the mounting point for?

  - Rotor blades and pitch change horns

- How is blade strength increased in the TH-57?

  - Bonding doublers and grip drag planes

- Where are blade weights added to the rotor blades?

  - Mid span and blade tips

- How many degrees of preconing is on the yoke?

  - 2 ¼

- The flap restraint assembly prevents damage to what part of the aircraft at low rotor RPM?

  - Tailboom

- What is the normal operating system pressure of the rotor brake?

  - 100-120 psi

- Between what range of Nr should the rotor brake be engaged?

  - 30-38 %

- What are the main components of the tail rotor system?

  - Rotor blades, pitch change horns, cross head, control tube, balance wheel, static stop, and yoke assembly

- What are the tail rotor blades made of?

  - Aluminum honeycomb with stainless steel skin

- What limits tail rotor flapping?

  - Static stops

- Why and how much is the tail rotor trunion offset?

  - Less than 90 degrees to remove geometric imbalance

- What is used to dynamically balance the tail rotor?

  - Balancing wheel

- What are the 3 flight controls?

  - Cyclic, Collective, anti-torque pedals

- How are the control inputs from the cyclic transmitted to the mixing lever?

  - Through a single yoke

- What do the rotating controls consist of?

  - Rotating swash plate, pitch change tubes, pitch change horns

- What is the uni-ball?

  - The mounting point for the stationary swashplate

- What is the hydraulic reservoir capacity?

  - 1 quart

  - 2 quarts

  - 1 pint

  - 3/8 pint

- Hydraulic pressure is regulated to ________ psi.

  - 650- 750 +/- 50

  - 600 +/- 50

  - 650- 750 +/- 30

  - 600 +/- 30

- The hydraulic pressure light illuminates below _____ psi and extinguishes above ____ psi.

  - 300, 400

  - 400, 300

  - 400, 600

  - 650, 750

- The hydraulic system is powered by

  - Tail rotor drive shaft

  - Electrical system

  - Transmission accessory drive shaft

  - Engine bleed air system

- DC power is required to turn off the hydraulic system.

  - True

  - False

- The force trim system

  - Eliminates feedback from the main rotor

  - Provides artificial feel for the cyclic

  - Eliminates feedback from the main rotor and tail rotor

  - Provides artificial feel for the cyclic and collective

- In the event of hydraulic system failure, your first action should be to

  - Adjust airspeed

  - Land

  - Autorotate

  - Ensure hydraulic boost off

- Operation of the force trim system requires

  - DC power

  - AC power

  - DC and AC power

  - No electrical power if hydraulic boost is on

- To aid in cooling the hydraulic reservoir, cooling air is directed from

  - Front engine mount

  - DC powered fan mounted on the bulkhead

  - ECS system

  - Engine oil cooler blower

- The force trim system is activated

  - By the top button on the cyclic

  - By the middle button on the cyclic

  - Automatically when the hydraulic boost is on

  - Automatically when the hydraulic system pressure rises above 400 psi

- Hydraulic system circuit breakers

  - Are not accessible from the cockpit

  - Remove hydraulic pressure from the hydraulic servo actuators

  - Will open if the system filter becomes clogged

  - Are in different positions in the B and C models

- Normal hydraulic system pressure is

  - 300

  - 400

  - 500

  - 600

- Hydraulic system pressure is read

  - Within the reservoir

  - Between the reservoir and the filter

  - Downstream of the filter

  - Within the collective servo actuator

- What is the purpose of the hydraulic system?

  - Reduce pilot workload

- What are the primary components of the hydraulic system?

  - Power pack, solenoid valve, servos, filter and pressure switch

- What does the Power pack consist of?

  - Reservoir, pump, pressure regulator valve, rotor tach gen, and mounting pad

- What are the major components of the servo actuator?

  - Sequence valve, pilot valve, and differential relief valve

- What admits ambient air into the ventilation system?

  - Axial blower

  - Flapper valve

  - Defroster nozzle

  - Electric fan

- What compensates for the lack of ram air in a hover?

  - Axial blower

  - Flapper valve

  - Defroster nozzle

  - Electric fan

- The tail rotor driveshaft is connected by a drivebelt to the

  - Condenser

  - Evaporator

  - Compressor

  - Compressor fan

- In the old bravo, relative humidity of the ambient air is reduced by _____ percent during the heat transfer stage.

  - 25

  - 30

  - 50

  - 75

- The defog system works best in conjunction with

  - Ventilation system

  - Flapper valve

  - Bleed air heater

  - Evaporator

- What does the air condition system consist of?

  - Engine driven compressor, condenser, condenser blower, evaporator, evaporator blower, switches

- How much power does the engine driven compressor take from the engine?

  - 5 HP

- What operates when the ECS switch is in fan?

  - Forward blowers and evaporator fan

- What powers the old bravo’s ECS?

  - Compressor Bleed air

- What is one advantage of the old bravo’s ECS?

  - It doesn’t require a separate heating system

- The five major components to supply ambient air to the cockpit and windscreen are?

  - Grill, flapper valve, axial blower, defroster nozzle, and vertical control knobs

- What is the power rating of the generator?

  - 30 VDC, 150 ampere hours

  - 28 VDC, 105 ampere hours

  - 24 VDC, 117 ampere hours

  - 150 VDC, 28 ampere hours

- Which of the following does the reverse current relay perform?

  - Connects the generator to the common BUS only when the proper voltage is obtained

  - Prevents current flow from the generator to the battery

  - Disconnect the generator from the common bus when voltage climbs above a safe level

  - Maintains the variable current at a stable 100 ampere hours

- What are the three power sources for the TH-57B?

  - Battery, Standby generator, Main generator

  - Starter/generator, external battery, auxiliary power unit

  - Main battery, standby battery, main generator

  - Starter/generator, battery, and external power unit

- What are loadmeter and voltmeter indications of a generator failure?

  - Loadmeter 22-24 Volts / Voltmeter 0

  - Loadmeter 0 Volts / Voltmeter 22-24

  - Loadmeter less than 50 Volts / Voltmeter less than 32

  - Loadmeter 100 Volts (full) / Voltmeter normal generator voltage

- When does the over voltage relay trip to generator reset?

  - When the line voltage reaches 28 +/- 0

  - When the line voltage reaches 31 +/- 1

  - When the line voltage reaches 31 +/- 0

  - When the line voltage reaches 28 +/- 1

- What action should be taken with generator failure or battery off or exhausted and why?

  - Descend below 6000 feet PA and Land as soon as possible: both fuel boost pumps are inoperative

  - Land as soon as possible: engine igniters will not sustain engine power without electricity

  - Land as soon as practical:  UHF / VHF have limited time on battery power

  - Land as soon as practical:  the pilots attitude indicator will display accurate data for only 6 minutes after power failure

- What are the power requirements for external starts?

  - 32 VDC, 105 ampere hours

  - 32 VDC, 150 ampere hours

  - 23 VDC, 400 ampere hours

  - 28 VDC, 400 ampere hours

- Sustained loadmeter indications above 70%

  - May be caused by and electrical fire

  - Are normal

  - Indicate voltmeter failure

  - Are normal when operating on external power

- When do the igniters receive power?

  - When the field control relay completes the circuit from the common BUS to the igniter and keeps these circuits connected until engine reaches self sustaining RPM

  - When the field control relay completes the circuit from the common BUS to the igniter and keeps these circuits connected until engine reaches self sustaining RPM, and the starter switch is released

  - Anytime Ng section is running

  - Anytime the common BUS is powered from the battery or external power unit

- The battery temp light illuminates when the battery case reaches ____ +/- ___ C, and the battery hot light illuminates when the battery case reaches ____ +/- ___ C.

  - 54, 3, 60, 3

  - 60, 3, 54, 3

  - 54, 0, 60, 0

  - 54, 10, 60, 10

- What type of battery is used in the TH-57B

  - Non vented lead acid battery

  - Vented alkaline battery

  - Vented nickel-cadmium battery

  - 18 self contained, 1.25 volt nickel cadmium dry cells

- What is the purpose and location of the common bus?

  - Connects battery power to the external power receptacle and is located in the battery compartment

  - The distribution point for electrical equipment and is located behind the overhead circuit panel

  - Connects the battery relay through the battery switch and is located in the overhead console

  - Completes the switch circuit of the battery relay to ground and is located on the electrical equipment shelf

- What is the power rating of the battery?

  - 24 VDC, 17 ampere hours

  - 17 VDC, 24 ampere hours

  - 24 – 17 VDC, 100 ampere hours

  - 24 VDC, 32 ampere hours

- What causes the generator to act as the starter?

  - The starter switch provides reverse DC power to the starter /generator and powers the igniters

  - With the starter relay activated, the standby generator shunt field is opened

  - With the starter relay activated, the generator shunt field is opened and the generator works as a starter

  - With the starter relay activated, the reverse current relay reverses the current to the generator fields and the generator works as a starter

- Which of the following are components of the generator system

  - Battery relay, voltmeter shunt, loadmeter C/B, and starter switch

  - Reverse current relay, engine Ng section, voltage regulator and AC common bus

  - Over – voltage relay, generator field relay, loadmeter shunt and generator field reset

  - Under – voltage relay, base – voltage regulator, ESS BUS and starter shunt

- What switch allows the crew to transmit over a selected radio?

  - Hot mike switch

  - Cyclic trigger switch first detent

  - Foot switch

  - Cyclic trigger switch second detent

- Which switch controls volume on the UHF radio?

  - Large knob on freq set

  - Small knob on freq set

  - Off/pull test

  - Switch mounted on headset

- HSI course select knob is used to position the course pointer to ?

  - Corrected magnetic compass heading

  - Indicated course from standby compass

  - Desired TACAN radial

  - Desired VOR radial

- What is the indication that the HSI is receiving unreliable information from the NAV 1 receiver?

  - Warning tones over ICS

  - Compass warning flag

  - NAV flag

  - Heading flag

- What piece of equipment produces radio input to the RMI?

  - UHF radio

  - VOR NAV radio

  - Transponder

  - GYRO

- What communication console switch is used for VOR reception?

  - AUX

  - NAV

  - Switch 1

  - Switch 2

- What switch on the UHF radio allows the crew to monitor both guard and a selected channel frequency at the same time?

  - Function selector switch

  - ADF switch

  - Guard

  - Feature not available on UHF radio installed in TH-57B

- The searchlight, landing light, defog blower, ECS, and pitot heat should be secured prior to checking what system component?

  - RMI deviation

  - Gyro alignment

  - Magnetic compass alignment

  - NAV / Receiver

- What position should the transponder be set on to transmit a selected code on Mode 3/C?

  - ALT

  - ON

  - TEST

  - STBY

- What component of the HSI provides a visual reference for the helicopters magnetic heading as indicated by the compass card?

  - Lubber line

  - Course select pointer

  - Heading select knob

  - To – From indicator

- What EP step should be performed for gyro instrument failure?

  - Shift scan to standby compass

  - Shift scan to secondary gyro

  - Reset DC generator bus

  - Land as soon as possible

- What is the indication of power interruption to turn slip indicator?

  - Caution light

  - Red warning flag

  - Tone over ICS

  - NAV flag

- Descent below the altitude set in the radar altimeter causes the ______ -________ to illuminate and actuates a/an __________.

  - Warning flag, emergency signal

  - Caution light, auxiliary signal

  - Altitude select, audible tone

  - DH lamp, warning tone

- What is the UHF guard frequency?

  - 243.0 kHz

  - 243.0 MHz

  - 255.0 kHz

  - 255 MHz

- What are the power requirements for engine start utilizing external power (Charlie Model)?

  - Same as the TH-57B.  DC power from the external power unit provides electrical power to all three buses.

  - Same as the TH-57B.  DC power from the external power unit provides electrical power to the essential buses

  - Same as the TH-57B.  DC power from the external power unit provides electrical power to the engine start bus

  - Same as the TH-57B.  DC power from the external power unit provides electrical power to all three DC buses and to the AC power system

- Why is the main generator switch moved to the reset position before placing it in the ON position?

  - Energizes the generator relay and connects the generator to ESS bus 1

  - De-energizes the generator relay and connects the generator to the essential and non-essential bus

  - De-energizes the standby generator, enabling the main generator to provide current

  - Provides excitation current to generator field, enabling the generator to provide current.

- The standby battery is capable of powering

  - Only the pilot’s attitude gyro, only in case of complete loss of power to ESS Bus 2

  - Only the pilot’s attitude gyro, only in case of complete loss of power to ESS Bus 1

  - Only the pilot’s attitude gyro, only in case of complete loss of power to AC systems

  - Only the pilot’s attitude gyro, only in case of complete loss of power to engine start system

- Describe the standby battery

  - The main battery is a 24VDC 17 ampere hour nickel cadmium battery

  - The standby battery is a 22.5 VDC 1.8 ampere hour power source

  - The main battery is a 24VDC 17 ampere hour nickel alkaline battery

  - It consists of 18 self contained 22.5 VDC nickel cadmium dry cells and a charging unit

- How do the main battery heat sensors work in the TH-57C?

  - The same as in the TH-57B

  - The same as in the TH-57B, except temperatures are different

  - Since the main battery is nickel cadmium, there’s no overheat sensor in the TH-57C

  - Monitored by battery protection circuits on equipment shelf

- What are the functions of the standby voltage regulator?

  - Is a solid state fixed regulator that obtains power from the standby generator

  - Provides only under / over voltage protection

  - Provides under / over protection, short circuit protection, and proper system voltage

  - Provides on short circuit protection, and proper system voltage

- What is the RCB remote control C/B

  - An ambient temperature sensor located between the battery and the battery relay

  - A bi-metallic overload sensor located between the generator and the voltage regulator

  - And overload sensor located between the battery in the battery relay

  - An ambient temperature sensor that will sustain a current load of 125 amperes

- What is the RCB override circuit?

  - It insures the RCB will trip during starts utilizing the battery only

  - It helps the RCB to take power away from the starter when engine start is accomplished

  - It prevents the RCB from taking power away from the starter before a complete start is accomplished

  - When the starter switch is turned on, the battery relay caution light will go out indication that the RCB circuit is being bypassed

- With the normal / recover switch in normal, failure of the main generator will result in the illumination of the Fuel Pump Caution light because of

  - Loss of power to ESS buses

  - Loss of power to non essential buses

  - Loss of power to the boost pumps

  - Loss of power to the fuel metering system

- Illumination of the STBY BAT ON caution light indicates that

  - Standby battery switch is on

  - Standby attitude gyro switch was left on after all other power turned off

  - Standby battery is powering the standby attitude gyro

  - The main battery has failed

- The power sources for the TH-57C are

  - Battery, standby battery, generator, standby generator, and APU

  - Battery, generator, EPU

  - Battery, generator, standby generator, EPU

  - Battery, standby battery, generator, standby generator, and EPU

- What of the following are associated with a main generator failure?

  - Loadmeter indicates zero

  - GEN FAIL caution light flashes

  - DC voltmeter drops to zero

  - STBY BAT ON caution light illuminated

- What is the purpose of the AC power system

  - The avionics inverter works with the avionics, FCS yaw axis and FCS

  - The inverters change 28 VDC current to 400 Hz, 115 VAC and 26 VAC

  - The AC power inverters generate power for the FCS

  - The inverters change 28VDC current to 400 Hz, 115 VDC and 26VDC

- What is the maximum number channel available for tuning on the KY –196 UHF radio?

  - 200

  - 350

  - 600

  - 720

- What component of the avionics system supplies input to the CDI?

  - Attitude gyro

  - NAV 2 receiver radio

  - KR-87 ADF

  - NAV 1 radio receiver

- Selecting the NAV1 button on the audio control panel

  - Indicates the way point elapsed time counter

  - Allows reception of VOR CW signals

  - Permits the pilot to select localizer or VOR inputs to NAV instruments

  - Switches NAV input from UHF to VHF

- What is the maximum operation range of the KR-87 ADF

  - 50-100 miles

  - 00-150 miles

  - 150-200 miles

  - 200-250 miles

- DME channels are selected by means of

  - KNS-81

  - Copilots ICS radio control panel

  - KDI-573 slaved receiver

  - Pilots ICS radio control panel

- The KDI-572 and KDI-573 DME/TACAN receivers normally display

  - Range to next way point and selected VOR frequency

  - Elapsed time and radials from way point

  - Station ID, the radial and time to selected VOR

  - Distance, ground speed and time to station

- What is the function of the avionics master switch?

  - Enables the gyro input to regulate avionics

  - Controls electrical power to associated avionics

  - Allows the KNS –81 system to be aligned with the gyro

  - Establishes a baseline start point for onboard NAV system way point frequency

- What is the frequency range for the KY –196 UHF radio?

  - 90 to 105.5 MHz

  - 118 – 135.95 MHz

  - 142.90 to 178.95 kHz

  - 140.80 to 187.93 MHz

- Where are the visual indications displayed on the marker beacon system when the aircraft passes over marker beacon at an ILS / LOC approach?

  - Pilot’s KR-21 and copilots KA –40

  - Pilot’s KR-40 and copilots KA –21

  - Copilots KR-21 adapter unit

  - Pilots KA-40 adapter unit

- That data is automatically displayed on the KNI –582 CDI?

  - VOR/ADF magnetic bearing and the magnetic bearing of the aircraft

  - VORTAC radio and aircraft TO- FROM bearing

  - Ground speed and radial to selected way point

  - Ground speed, way point radials elapsed time

- What control button on the KNS-81 NAV 1 receiver causes a displayed way point to become the active waypoint and moves the caret display to the frequency mode?

  - RAD

  - RTN

  - USE

  - CHK

- How are the lights tested on the KR-21 marker beacon?

  - Depress on/off switch

  - Pull on/off switch

  - Select sensitivity switch T position

  - Depress indicator light button

- What is the function of the CDI omni-bearing selector?

  - Allows input of 10 way points

  - Selects strongest VOR signal for display

  - Indicates deviation from selected waypoint radial when switch is depressed

  - Drives the course deviation card for course selection

- What must be selected on the KTU- 709 DME/TACAN system audio control panel for station ID?

  - VOR

  - VORTAC

  - DME

  - RAD

- Where are the controls located for the rear seat communication receiver located in the TH-57C?

  - Aft bulkhead passenger compartment

  - Top row of buttons on pilots audio control panel

  - Bottom row of buttons on pilots audio control panel

  - Top row of buttons on the copilots audio control panel

- What avionics system allows the option of tuning in transcribed whether or AM commercial radio broadcasts?

  - KTU-709 DME / TACAN

  - KRU –87 NAV / ADF

  - KDI – 206 CDI

  - KNS – 81 NAV 2 receiver

- When the KNS-81 RAD button is depressed in the RNAV mode what information is displayed?

  - Ground speed

  - Elapsed time to way point

  - Radial from VOR station

  - Radial from way point

- With a TACAN station selected on NAV-1 of the KNS-81, TACAN bearing is active on the HSI and the

  - Single needle of both RMI’s

  - KDI-572 indicator display

  - KDI-573 slaved indicator

  - Double needle of both RMI’s

- What is one indication of a failure in the ICS / radio selector panel

  - Illumination of the ICS/radio caution light

  - Warning tone in pilots headset

  - Tripped comm C/B

  - Loss of side tone

- Depressing the FCS button on the cyclic grip will

  - Engage the altitude hold

  - Reset the FCS OUT caution light

  - Initiates the FCS systems test

  - Turn the system OFF if it is ON or ON if it is OFF

- MINISTAB electrical power requirements are

  - 28VDC, 26VAC, 115VAC

  - 26VDC, 28VAC, 115VAC

  - 28VDC, 26VAC, 110VAC

  - 26VDC, 28VAC, 110VAC

- In the TH-57C, if airspeed, altitude and/or VSI behave erratically, your first action should be

  - Pull static air source knob

  - Turn on pitot heat

  - Turn off ECS

  - Land as soon as practical

- MINISTAB system C/B’s

  - Are not accessible to the pilot

  - Are located on the overhead panel

  - Are located on the pedestal panel

  - Are located on both the overhead and pedestal panels

- The FCS OUT caution light illuminates for approximately ____ seconds if the altitude hold is momentarily turned off or disengaged

  - 2

  - 3

  - 5

  - 10

- Once you stop moving the controls and movement has stabilized below 1.5 degrees per second, _____ later the ICO is secured.

  - 9 seconds

  - 9 milliseconds

  - 900 milliseconds

  - 90 nanoseconds

- A temperature switch to turn the system off in the event the motor overheats is installed on

  - All electromechanical actuators

  - Yaw electromechanical actuator

  - Pitch and roll electromechanical actuators

  - Pitch electromechanical actuator

- The MINISTAB system has a total of _____ -_____ actuators

  - 3 hydraulic

  - 3 electromechanical

  - 4 hydraulic

  - 6 electromechanical

- On the TH-57C the alternate static air source vent is

  - Located on the pilots window

  - Located under the pilots seat

  - Located under the copilots seat

  - Not installed on the Charlie model

- Altitude errors of more than ______ feet will disengage the altitude hold

  - 100

  - 150

  - 200

  - 250