TH-57 FUEL PLAN

1.	RESERVE FUEL

20 MIN BURN AT CRUISE FF	     9

2.	REQUIRED FUEL

FUEL TO DEST IAF	46

FUEL FOR DEST APP	0

FUEL TO ALTN IAF	0

FUEL FOR ALTN APP	0

RESERVE FUEL	9

MINIMUM ON DECK FUEL	10

TOTAL FUEL REQUIRED	65

(GO-NO-GO FUEL)

3.	EXTRA FUEL \ TIME AT CRUISE FF

EST TAKEOFF FUEL	88

MINUS FUEL REQUIRED	65

EXTRA FUEL	23

EXTRA TIME	0+53

- FUEL ON BOARD

TIME TO DEST IAF		1+30

TIME FOR DEST APP		0

TIME TO ALTN IAF		0

TIME FOR ALTN APP		0

RESERVE TIME		20

EXTRA TIME		0+53

TOTAL TIME		2+43

FLIGHT LOG

| DEP ELEV NDZ 178’ | CLNC DEL CH 2 | GND CONT CH 3 | TOWER CH 4 |
| --- | --- | --- | --- |
| ALT CORR 1000’ MSL | TIME OFF | TAS 100 KTS GS | LBS PH/MIN 26 GPH |
| CLEARANCE |  |  |  |
| DEPARTURE |  |  |  |
| DEST ELEV | APC CONT | TOWER | GND CONT |
| ROUTE | IDENT | CUS | DIST | ETE | ETA | LEG FUEL | EFR | GS | NOTES Lat / Long |
| TO | CHAN |  |  |  | ATA |  | AFR |  |  |
| PT 1 |  | 258 | 4 | 2:18 |  | 1 | 64 | 100 | N 030O 41.6’ |
| PT BAKER |  |  |  |  |  |  |  |  | W 087O 03.7’ |
| PT 2 |  | 259 | 10 | 6:00 |  | 3 | 61 | 100 | N 030O 40.8’ |
| POND CRK |  |  |  |  |  |  |  |  | W 087O 07.7’ |
| PT 3 |  | 348 | 4 | 2:29 |  | 2 | 59 | 100 | N 030O 39.1’ |
| 3-WY INT |  |  |  |  |  |  |  |  | W 087O 19.2’ |
| PT 4 |  | 005 | 9 | 5:27 |  | 3 | 56 | 100 | N 030O 43.0’ |
| MOLINO XRD |  |  |  |  |  |  |  |  | W 087O 20.3’ |
| PT 5 |  | 278 | 8 | 5:05 |  | 3 | 53 | 100 | N 030O 52.8’ |
| McDAVID |  |  |  |  |  |  |  |  | W 087O 19.4’ |
| PT 6 |  | 228 | 17 | 10:27 |  | 5 | 48 | 100 | N 030O 53.6’ |
| GRAIN ELEV |  |  |  |  |  |  |  |  | W 087O 28.9’ |
| PT 7 |  | 126 | 7 | 4:24 |  | 2 | 46 | 100 | N 030O 41.9’ |
| STEEL WD LK |  |  |  |  |  |  |  |  | W 087O 43.8’ |
| PT 8 |  | 116 | 7 | 3:52 |  | 2 | 44 | 100 | N 030O 37.6’ |
| I-10 OVRPS |  |  |  |  |  |  |  |  | W 087O 37.0’ |
| PT 9 |  | 096 | 5 | 2:43 |  | 2 | 42 | 100 | N 030O 34.9’ |
| STYX RVR |  |  |  |  |  |  |  |  | W 087O 30.3’ |
| PT 10 |  | 130 | 3 | 1:50 |  | 1 | 41 | 100 | N 030O 34.6’ |
| I-10 BND |  |  |  |  |  |  |  |  | W 087O 24.8’ |
| PT 11 |  | 073 | 10 | 6:21 |  | 3 | 38 | 100 | N 030O 32.6’ |
| SITE 8 |  |  |  |  |  |  |  |  | W 087O 22.3’ |
| PT 12 |  | 083 | 5 | 3:12 |  | 2 | 36 | 100 | N 030O 35.7’ |
| INT 90-197 |  |  |  |  |  |  |  |  | W 087O 10.4’ |
| PT 13 |  | 123 | 5 | 3:00 |  | 2 | 34 | 100 | N 030O 36.2’ |
| PT WHISKEY |  |  |  |  |  |  |  |  | W 087O 04.4’ |
| PT 14 |  | 035 | 4 | 2:24 |  | 2 | 32 | 100 | N 030O 33.6’ |
| YLW RVR |  |  |  |  |  |  |  |  | W 086O 59.3’ |
| PT 15 |  |  |  |  |  |  |  | 100 | N 030O 36.6’ |
| SANTA ROSA |  |  |  |  |  |  |  |  | W 086O 56.7’ |
|  |  |  |  | 59:32 |  | 33 |  |  |  |
| OPS @ |  |  |  | 30 |  | 13 | 19 |  |  |
| SANTA ROSA |  |  |  |  |  |  |  |  |  |

# Text boxes

##### Departure to Destination

TAS

Climb

Cruise

Approach

Altitude

Cruise

Avg Climb

Avg Descent