BIRD STRIKE CHECKLIST

SUSPECTED BIRD STRIKE

- NOTE ANY UNUSUAL VIBRATIONS

- LAND AS SOON AS POSSIBLE.

AFTER LANDING

- NOTE ANY 1 PER/REV VIBRATIONS AT 100% NR.

AFTER SHUTDOWN

- IF POINT OF IMPACT IS KNOWN INSPECT THAT PORTION OF THE AIRCRAFT FIRST.

- INSPECT THE FOLLOWING AREAS:

  - ALL EXTERNAL SURFACES FOR ANY VISIBLE DAMAGE: DENTS, DISTORTIONS, SCRATCHES, NICKS.

  - ALL EXPOSED FLIGHT CONTROLS. PAY PARTICULAR ATTENTION TO THE PITCH LINKS.

  - ENGINE INLET FOR ANY INDICATION OF FOD OR OTHER DAMAGE.

  - HORIZONTAL AND VERTICAL STABILIZERS FOR SKIN CRACKS AND FOR ANY LOOSENESS ON THE TAILBOOM.

  - MAIN ROTOR AND TAIL ROTOR BLADES.

- PERFORM NORMAL START WITH PARTICULAR ATTENTION PAID TO FLIGHT CONTROL CHECKS.

- PERFORM A 5 MINUTE 100% NR GROUND RUN NOTING NORMAL ENGINE OPERATION.

IF VISIBLE DAMAGE OR UNUSUAL VIBS ARE DETECTED, THE AIRCRAFT WILL BE RECOVERED BY MAINTENANCE. IF NO DAMAGE/VIBS ARE NOTED THE AIRCRAFT CAN BE FLOWN BACK TO SOUTH WHITING FOR A MAINTENANCE INSPECTION.