SUSPECTED HARD LANDING /

TAIL STRIKE CHECKLIST:

- Shutdown the aircraft.

- Inspect the main rotor mast for indentations at static stop contact area.

- Inspect the static stops for deformation.

- Inspect the main rotor blades for damage.

- Inspect landing gear skid tubes and cross tubes for damage, distortion, and deflection. Inspect the cross tube attachment points.

- Inspect the spike plate for sheared or loose rivets.

- Inspect isolation mount for contact with the main drive shaft coupling.

- Inspect the cowling access doors and crew compartment doors for proper fit and alignment.

- Inspect the tail boom, fuselage exterior, and bathtub area for buckling or excessive waviness. Inspect the upper tail boom attach fittings.

- Inspect the tailskid and mounting for looseness or damage.

- Inspect the tail rotor blades for damage.

- Check the  flight controls for smooth operation and proper swash plate deflection.

- Inspect the Nr tach-generator and surrounding components and structure for damage.

- Inspect fuel, oil, and hydraulic system for damage/leaks.

- If no damage is found, start engine and check main rotor at flat pitch has no 1 per vibrations.

- If visible damage or unusual vibes are detected, the aircraft shall be recovered by maintenance. If no damage/vibes are noted the aircraft can be flown directly back to South Whiting for a maintenance inspection  following receipt of permission for a one time Might from  the Commodore, Wing Operations Officer, or Wing Maintenance Officer. In a case of uncertainty or anytime the pilot in command has reservations, maintenance shall recover the aircraft.