T-34 Limitations

Operating limits: ITT

Normal idle range			400-660°C

Normal operating range		400-695°C

Max @ shutdown w/cond.lever	610°C

Max continuous			695°C

Max acceleration			825°C

Hot start				925°C (2 sec)

Max during starts			1090°C

Prop RPM (N2)

Idle operating range		<1800RPM

Normal operating range		2200 RPM ±25

Over speed governor		2332 RPM ±40

Fuel topping governor		2398 RPM

Engine Tachometer (N1)

Introduce fuel			@ 12%

Flameout				10-12%

FCU stuck @min.flow(rollback)	40-60%

Minimum for flight (griped)	60%

Idle operating range		62-65%

Normal operating range		89-93%

Maximum				101.5%

Max acceleration			102.6%

Airspeed Limitations

Max clean (surface-20,000’)	280 KIAS

(20,000- 25,000’)	245 KIAS

Max canopy emergency open	250 KIAS

Max canopy open			240 KIAS

Max turbulent air penetration	195 KIAS

Max gear extension		150 KIAS

Max flap extension		120 KIAS

Max gear retraction		120 KIAS

Min flap retraction		90 KIAS

Downwind airspeed			100 KIAS

VFR/overhead break airspeed	170 KIAS

Full flap landing airspeed	85 KIAS

No flap landing airspeed	95 KIAS

Best angle of climb (Vx)	75 KIAS

Best rate ot climb (Vy)		100 KIAS

Recommended bailout airspeed	90-120 KIAS

Max range airspeed		580 ft-lbs

Max endurance airspeed		420 ft-lbs

Torque

Idle operating range		150 ft-lbs

Auto ignition range		300-180…

Descent				300…

Prop over speed test range	400-500…

Normal operating range		400-l015…

Climb					1015 (695°C)

Max allowable			1015…

Maximum torque			1315…

Max torque (oil malfunction)	850…

Fuel Flow

Idle					~125 lbs/hr

Normal operation			~335 lbs/hr

Oil Temperature

Min starting temperature	-40°C

Normal Operating range		10-99°C

Maximum				100°C

Oil pressure

Idle operating range		40 PSI min

Normal operating range		65-85 PSI

Maximum fluctuation		+5 (within limits)

Max oil pressure			100 PSI

G Limits

Up to 280 KIAS			+4.5/-1.0 G's

Up to 220 KIAS			+4.5/-2.3 G's

Flaps down				+2.0/-1.0

Time limits

Max time inverted			15 sec

Max time vertical (nose up)	15 sec

Max time vertical (nose down)	3 sec

Max time wings vertical (knife edge):3 sec

“Zero G” condition		transient

Starter		40s/60s/40s/60s/40s/30min

Dimensions:

Wing span				33’ 5”

Length				28’8”

Height (at rest)			9’11”

Tread					9’6”

Prop arc clearance		11”

Weight limitations

Maximum ramp weight 		4,425 lbs

Takeoff and landing 		4,400 lbs

Max aerobatic weight 		4,300 lbs

Max zero fuel weight 		3,650 lbs

Approximate basic weight	~2,970 lbs

Miscellaneous limits

Max sink rate @ touch down	600 FPM

Max crosswind component	22(NF),15(FF)

Max operating altitude		25,000’

Air start envelope, SL-20k’	80-280 KIAS

Engine: Pratt & Whitney PT6A-25

Flat rated				550 SHP(1315)

Normal operation			425 SHP(1015)

Landing Gear

Nose gear turn limits		±30°

Main tire pressure		90 PSI ± 2

Nose wheel tire pressure	70 PSI ± 2

Oxygen system capacity		1850 PSI@70°F

Oxygen system volume		76 cubic feet

Oil system capacity		4.4 gal

Oil tank capacity			2.8 gal

Usable oil	(upright)		1.4 gal

(inverted)		.25